ANEXO 05 – SIS TEL UHF PARK AIR

Tabela de configurações dos rádios VHF / UHF ParkAir

TRANSMISSOR			RECEPTOR
Standby	OFF		Standby	OFF
LCD Backlight (Sec)	30		LCD Backlight (Sec)	30
Ready Output Polarity	STD		Ready Output Polarity	STD
Bit Initiate Input Pol	STD		Bit Initiate Input Pol	STD
EBIT Input Polarity	STD		EBIT Input Polarity	STD
Front Panel Lock	OFF		Front Panel Lock	OFF
HDLC Lock	OFF		HDLC Lock	OFF
T1E1 Lock	OFF		T1E1 Lock	OFF
MARC Lock	OFF		MARC Lock	OFF
Power (W)	50		RF Pre Atten	OFF
Ext VSWR Input Polarity	STD		Inhibit	OFF
Inhibit	OFF		Inhibit Input Polarity	STD
Inhibit Input Polarity	STD		Step Size (kHz)	25
Step Size (kHz)	25		Squelch Level (dBm)	-107
Antenna CO Output Polarity	STD		Squelch Defeat	OFF
Antenna CO Delay	ON		Line Out Level (dBm)	-13
Mod Depth (%)	85		Squelch Carrier Override	OFF
Line In Level (dBm)	-13		Squelch Noise Compensation	ON
Local Ptt Enable	OFF		Squelch Defeat Input Pol	STD
Remote Ptt Enable	ON		FAC Squelch Output Pol	STD
Phantom Ptt Enable	OFF		MARC Squelch Output Pol	STD
Key Priority	LOCAL		Phantom Squelch Output Pol	STD
PTT Input Polarity	STD		RX Audio AGC	ON
Phantom PTT Input Polarity	STD		Loudspeaker	ON
PTT Output Polarity	STD		Volume (%)	0
Fast PTT Output Polarity	STD		RX Tone Signal Enable	OFF
PTT Reference Voltage (V)	-14		RX Tone Signal Freq (Hz)	1930
Transmit Timeout (Sec)	180		RX Tone Signal Level (dB)	-10
TX Mute	ON
TX VOGAD	ON
Microphone	PASSIVE
Offset Carrier Filter	OFF
PTT Confirm Config	ON
TX Tone Signal Enable	OFF
TX Tone Signal Freq (Hz)	2040
TX Tone Signal Level (dB)	-10